PS-28 Cruiser CHECKLIST PH-NEW     1

Preflight /Daily inspection	COMPLETED

Papers / Map………….......	CHECKED/ON BOARD

Loose objects…………….	SECURED

Circuit breakers …….……  CHECK ALL IN

Seat Belts	…………………	FASTEN

Rudder pedals………….…	ADJUSTED/SECURED

Fuel Caps/Wing Lockers..  IN PLACE / CLOSED

Canopy……………………...	CLEAN, CLOSED & LOCKED

Master Bat …………………	ON

Master Gen………………...	ON

EMS………………………….	ON

Avionics …………………...	ON

Nav lights………………….	ON

Strobe lights ………………	ON

Parking Brake ……………	ON

Carb heat ………………….. OFF

Fuel Selector ……………..	LEFT TANK

Fuel pump	 …………………	ON - CHECK PRESSURE

Choke ……………………...	AS NEEDED

Throttle …………………….	JUST OPEN

Propeller Area ……………	CLEAR

Start Engine ………………	TURN KEY TO START

Oil Pressure ………………	CHECK 2-7 BAR

Choke ……………………...	GRADUALLY RELEASE

Versie: 17 September 2022

2   PS-28 Cruiser CHECKLIST PH-NEW

Engine RPM ………….…… MAX. 2500 RPM FOR                                                                                                                                  	                                     WARMING UP (OIL < 50°C)

Fuel pump	 …………………	OFF

Altimeters	…………………. SET (Both)

Transponder……………....	STANDBY 7000

Weight & Balance………..	SET ON GARMIN (Check Limits)

Radio…………………….….	CHECK ON

Intercom…………………....	CHECK ON

Flaps ………………….……	CHECK FULL TRAVEL,

RETRACTED (0°)

NOTE: DO NOT START TAXI UNLESS OIL TEMP HAS    REACHED 300 C

Oil Temp …………………..  MIN. 30°C

Wind direction …………...  CHECK (For runway in use)

Time ……………………….  CHECK (Start flight timing)

Radio call …………………	APPLY

Parking Brake ……………	RELEASE / CHECK BRAKES

PS 28 Cruiser CHECKLIST PH-NEW     3

Parking brakes …………...	ON

Fuel selector ……………..	RIGHT TANK

Engine instruments ……..	CHECK, WITHIN LIMITS

Ignition Check ………….... 	THROTTLE 4000 RPM

Test Ignition ………….…..	MAX. DROP 300 RPM

MAX. DIFF. 115 RPM

Carburetor Heat …….…...	PULL HOT, CHECK RPM DROP MAX. 100 RPM,

PUSH OFF

Engine instruments ……..	CHECK OIL AND FUEL PRESSURE

Throttle ………………….…	IDLE (1700-2000 RPM)

EFIS and EMS ……….…...	DISPLAY MAIN SCREENS

Elevator trim ……………...  SET 1/3 DOWN

Aileron trim  ………………  SET (check on right aleron)

Flight Controls ……….…..	FULL / FREE AND CORRECT

Flaps ………………….……	TAKEOFF POSITION (12°)

Fuel Selector ………….….	FULLEST TANK

Fuel pump……………….… 	ON

Landing Light …………….  ON

Ignition Switch ……….…..	KEY POSITION BOTH

Canopy …………………..... CLOSED & LOCKED

Parking brakes …………...	CHECK OFF

4   PS 28 Cruiser CHECKLIST PH-NEW

Wind……………………...… CHECK

Throttle …………………….	MAX (Min. 5000 RPM)

Engine Instruments ……..	WITHIN LIMITS

At 45 KT…………………….	ROTATE

Climb ………………………	65 KIAS (VX= 55KT)

AFTER TAKE - OFF

Brakes ……………………..	APPLY AFTER LIFT-OFF

Flaps ……………………….	RETRACT ABOVE 200’ AGL

Trims ………………………	AS REQUIRED

Fuel pump………………...   OFF AT SAFE ALTITUDE

Climb speed ……………..    75 KTS

Seat belts ……………….…	FASTEN

EMS ………………………..	MAIN SCREEN

Fuel Pump ………………...	ON

Landing Light …………….	ON

Carburetor heat .…………	PULL HOT

Fuel Valve ..……………….	FULLEST TANK

Airspeed …………………..	MAX. 75 KIAS

Flaps ……………………….	SET

Airspeed…………….….….	MIN. 60 KIAS

Brakes ……………………..	OFF / CHECK PRESSURE

Engine Instruments ……..  CHECK

PS 28 Cruiser CHECKLIST PH-NEW       5

Carburetor HEAT ..……….	OFF

Flaps ……………………….	RETRACT TO 12°

Fuel Pump ………………...	OFF

Landing Light …………….	OFF

Trims ……………………….	SET TO NEUTRAL

Parking Brake …………….	AS NECESSARY

Throttle ……………………	IDLE

Instruments ………………	WITHIN LIMITS

Time ……………………….   CHECK (Stop flight timing)

Avionics Switch …..……..	OFF

Ignition Switch …………..	OFF & REMOVE KEY

Strobe lights ……………..	OFF

Nav lights …………………  OFF

EMS……………………...…	OFF

Master GEN ………………	OFF

Master BAT ……………….  OFF

Fuel Selector ……………..	OFF

Check All Switches ….….	OFF

NOTE: Check all switches OFF after leaving the cockpit

6   PS 28 Cruiser CHECKLIST PH-NEW

PS 28 Cruiser Daily Inspection

1)	Canopy ………..	Condition of attachment, cleanness

Cabin ………….	Check for loose objects

Ignition …………	OFF, key removed

Master BAT ……	ON

EMS ……………	ON, Check battery voltage, EMS screen,

Fuel quantity

Avionics ……….	ON. Check EFIS, Transponder, Radio, Intercom and GPS

Lights ………….	ON. Check NAV, Strobe Landingslight,

Cockpit instr L&R

Flight Controls ...	Visual Inspection, function, free movement

Wing Flaps …….	Check function

Trims …………..	Check function

PS 28 Cruiser Daily Inspection

2)	Wing Flap ……..	Surface, Condition, Attachment and Clearance

Aileron …………	Surface, Condition, Attachment and Clearance,

Free movement, Trimtab surface and attachment

Wing Tip ………	Surface, Condition and Strobe/Nav light

3)	Wing Surface ….	Condition, Cleanness

Leading Edge …	Surface, Condition, Cleanness

Wing Locke …....	Closed and Locked

Pitot Head ……..	Condition, attachment, Cleanness

4)	Nose Gear …………….	Wheel, Fairing and Leg attachment,

Condition, Check pressure of Tire

Engine Cowling ………	Condition

Prop & Spinner ………	Condition

Engine Mount,

Exhaust Manifold …..	Condition, Attachment

Oil Quantity ………….	Check and replenish as required

Close Oil Tank

Coolant quantity ……...	Check

Fuel and Elec system ..	Visual Inspection

Fuel System ………….	Drain

5)	Main Landing Gear …..	Wheel Fairing, Leg and Brake attachment,

Condition, pressure of Tire

Fuselage surface …….	Condition, Cleanness

Antennas			Attachment

6)	Vertical Tail Unit ………	Condition of Surface, Attachment,

Free Movement, Rudder Stops

Horizontal Tail Unit ….	Condition of Surface, Attachment,

Free Movement, Elevator Stop

Trim Tab Surface & Condition, Attachment

Anti Balance Tab Surface, Condition,

Attachment

PERFORM WEIGHT AND BALANCE

# Text boxes

Before Engine Start

Engine Start

After Engine Start

Engine Limits:

Speed 			5800 rpm (5 min.)

5500 rpm (continuous)

Cyl. Head Temp.		90° – 135° C (135°C max.)

Oil Temp.			90°C - 110°C (130°C max.)

Exh. Gas Temp.		880°C max..

Oil Pressure			2 - 5 bar (7 bar max. cold eng.)

Fuel Pressure		0,15 – 0,4 bar

TAXI

ENGINE RUN-UP

BEFORE TAKEOFF

TAKEOFF

APPROACH AND LANDING

AFTER LANDING

AIRCRAFT PARKING

AIRCRAFT LIMITS

VNE never exceed	   		138 KTS

VA maneuvering			  88 KTS

Vno Max cruising speed		108 KTS

Vfe max flap 12°			  75 KTS

Vfe max flap 30°			  65 KTS

VX best angle climb		  55 KTS

VY best rate climb			  62 KTS

best economical climb		  75 KTS

Vs stall clean				  37 KTS

Vso full flaps				  31 KTS

Best glide speed			  60 KTS

Max. dem. crosswind		  12 KTS

Max. dem. headwind    	          24 KTS

G-limits flaps up			  +4 / -2

G-limits flaps down		  +2 /  0

Service ceiling		               15.090 FT

Empty weight					387 	   KG

Max baggage weight			  28 	   KG

Max. T/O weight				600	   KG

Max Forward CG Limit	420 MM	28%    MAC

Max AFT CG Limit		525 MM   35%    MAC

PS28 Cruiser EMERGENCY Procedures

ENGINE FAILURE DURING T/O RUN                .

Throttle ……………..	IDLE

Brakes ………………	APPLY

Ignition ……………..	OFF

ENGINE FAILURE AFTER TAKEOFF              .

Airspeed ……………	60 KNOTS

Flaps ………………..	AS NECESSARY

Fuel Selector ………	OFF

Ignition Switch …….	OFF

Master Gen …………	OFF

Master Bat ………….	OFF – BEFORE LANDING

Land straight ahead, turning only to avoid obstacles

LOSS OF ENGINE POWER IN FLIGHT            .

Speed ………………..	….	60 KIAS

Inflight Engine Restart ..	APPLY

OR PERFORM  EMERGENCY  LANDING

EMERGENCY DESCENT                      .

Airspeed …………………..	MAX PERMITTED:

VNE 	= 138 KIAS

Vno	= 108 KIAS

VA	=   88 KIAS

Engine RPM ……………….	MAX. 5800 RPM

PS28 Cruiser EMERGENCY Procedures

ENGINE FIRE DURING T/O RUN                 .

Fuel Selector ……….	OFF

Throttle ……………...	IDLE

Brakes ………………	APPLY AS NEEDED

When airplane is under control:

Fuel Pump ………….	OFF

Cabin Heating ………	OFF

Ignition ………………	OFF

Master BAT & GEN …OFF

Parking Brake ………	SET

Evacuate the aircraft!

ENGINE FIRE IN-FLIGHT                   .

Fuel Selector ………	OFF

Throttle ……………..	MAX

Cabin Heat …………	PUSH OFF

Ignition Switch …….	OFF AFTER ENGINE STOPS

Airspeed ……………	60 KIAS

Master Switch ……..	OFF

Perform emergency landing!

Airplane …………….	LEAVE

ELECTRICAL  FIRE  IN FLIGHT                 .

Master BAT & GEN …OFF

Other switches ……..	OFF

Cabin Heater ………..	PUSH OFF

Ventilation ………….	OPEN

PERFORM EMERGENCY LANDING  AS SOON  AS POSSIBLE

PS28 Cruiser EMERGENCY Procedures

IN-FLIGHT  ENGINE  RESTART                   .

All unnecessary electrical equipment ……. OFF

Master Bat ………….	ON

EMS …………………	ON

Fuel Pump ………….	ON

Fuel Selector ………  FULLEST  TANK

Throttle ……………..	IDLE

Ignition Switch …….	HOLD-START / BOTH

After engine is running

Master GEN …………	ON

Avionics …………….	ON

Fuel Pump ………….	OFF

Other Switches ……	ON AS NECESSARY

EMERGENCY LANDING  WITHOUT  ENGINE  POWER

Airspeed ……………	60 KIAS

Locate suitable terrain without obstacles

COMM ……………….	GIVE LOCATION & INTENTIONS

Ignition ………………	OFF

Fuel Selector …….…	OFF

Master GEN ………... 	OFF

Approach …………...	WITHOUT STEEP TURNS

Seat belts …………...	TIGHTEN

Flaps …………………	AS  NECESSARY

Master BAT …………	OFF BEFORE LANDING

PS28 Cruiser EMERGENCY Procedures

POWER-ON  FORCED  LANDING                    .

A precautionary landing is generally carried out in the cases where the pilot may be disorientated, the aircraft has no fuel reserve or possibly in bad weather conditions.

1. Choose landing area, determine wind direction.

2. Report your intention to land and landing area location.

3. Perform low-altitude passage into wind over the right-hand side of the

chosen area with flaps extended as needed and thoroughly inspect the

landing area.

4. Perform circle pattern.

5. Seat belts  - fasten

6. Perform approach at increased idling with flaps in landing position (30°) at

60 KIAS.

7. Reduce power to idle when flying over the runway threshold and

touch-down at the very beginning of the chosen area.

8. After stopping the airplane:

Ignition Switch - OFF

All switches - OFF

FUEL selector - OFF

Airplane - lock and seek assistance

RECOVERY FROM UNINTENTIONAL SPIN          .

Power ……………….	IDLE

Flaps ………………..	RETRACT

Ailerons …………….	NEUTRAL

Rudder ……………..	FULL OPPOSITE

Elevator …………….	PUSH FORWARD

HOLD THESE INPUTS UNTIL THE ROTATION STOPS THEN:

Rudder ………………	NEUTRAL

Elevator ……………..	PULL GENTLY TO

RECOVER FROM DIVE